## Slide 1
Amendment history of the template
Rev 版本 | Date 修改日期 | Details 修改原因及内容 | Owner 作者（名字 和职位） | Lenovo/Moto Approver 审批（名字 和职位）
1.0 | 17/06/2019 | Initiate version released | Tim.Peng | 
1.1 | 21/06/2019 | Add the description of each material and their Lenovo PN Add press force and dwell time for camera lens&side key FPC Add a type of screw Add shore hardness ,press force and dwell time of FPS press fixture | Tim.Peng | 
1.2 | 01/07/2019 | Add the press force and dwell time of Receiver Pressing | Tim.Peng | 
1.3 | 16/07/2019 | 1.Add one procudure:”Clean the camera lens adhesive area of rear housing with dust-free cloth dipped with ethanol” ---To make the camera lens more sticky to rear housing 2.Change the dwell time of camera lens pressing from 6--8S to 10--12S To make the camera lens more sticky to rear housing 3.Change the screw bit from PHOOO to PHO 4. Exchange the procedure sequence of 2M camera and main board screw protective film.Paste the films firstly,then assemble 2M rear camera---To avoid the interference between film and liner of 2M camera. | Tim.Peng | 
1.4 | 19/07/2019 | 1.Change the dwell time of camera lens pressing from 6--8S to 10--12S 2.Add the CCP in the file | Tim.Peng | 

## Slide 2
Assembly Checklist
Poker
Parent DOI #: 004.301.XXX
Document #: 004.301.XXX.001
Revision: 1.4
Revision Date: 19/07/2019
NPI Engineer: Tim.Peng
Review the following checklist steps and complete online acknowledgement before the start of each build.
NOTE: P/Ns SHOWN IN THIS DOCUMENT ARE FOR REFERENCE ONLY. FOR PART ORDERING , TRACKING, OR CONFIRMATION OF P/Ns, REFER DIRECTLY TO THE ENGINEERING BOM.
Use Moto model name here
Use 0.1 for EVT build, than 1.0 from the first build of DVT, after that should be 1.1, 1.2, 1.3… until MP
Use Moto model name here
Show the latest version in Amendment history
The date for this version
ODM author for this document
No need to update contents in blue

## Slide 3
 |  | Paste thermal conductive silicone,fastedn the RF and BB shield cover |  |  |  |  |  |  | 
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M716-BDD000-005 | CPU silicone tape/S948C58605 |  | 1
M716-BDD001-010 | DDR silicone tape/S948C57340 |  | 1
M716-BDD000-007 | PMIC silicone tape/S948C58609 |  | 1
M716-BDD000-006 | PA silicone tape/S948C58607 |  | 1
N207-BDD003-000 | BB shield cover/S948C55555 |  | 1
N206-BDD000-000 | RF shield cover/S948C55557 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pasting sponge@main board（Back） |  |  | 
Place the main PCBA on the fixture,paste 4pcs thermal conductive silicone in the corresponding position as shows as the picture.
Fasten the RF and BB shield cover as shows as the picture.
Paste 1PCS P160AN CPU thermal conductive silicone tape
Paste 1PCS P160AN DDR thermal conductive silicone tape
Paste 1PCS P160AN PMIC thermal conductive silicone tape
Paste 1PCS P160AN PA thermal conductive silicone tape
Fasten the RF shield cover
Fasten the BB shield cover

## Slide 4
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M709-BDD000-008 | FPS connector sealed foam/S948C56095 |  | 1
M709-BDD000-010 | Main FPC connector sealed foam/S948C55529 |  | 1
M709-BDD000-031 | Rear camera connector sealed foam/S948C58598 |  | 1
M709-BDD000-007 | side key connector sealed foam/S948C55837 |  | 1
M709-BDD000-005 | Front camera connector sealed foam/S948C55835 |  | 1
M709-BDD000-001 | Earphone socket sealed adhesive@MB/S948C55818 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pasting waterproof foam@MB |  |  | 
Paste the connector sealed foams on PCBA as shows as the picture below
Paste 1pcs earphone socket sealed adhesive
Paste side key FPC connector sealed foam
Paste 1pcs "P160AN Front camera connector sealed foam"
Paste 1pcs"P160AN rear camera connector seal foam"
Paste main FPC connector sealed foam
Paste finger print connector sealed foam

## Slide 5
Buckle the RF coaxial cable
Paste the BB nano carbon copper foil
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
EI06-320807-002 | RF coaxial cable/S948C55544 |  | 1
M721-BDD001-004 | main board BB nano copper foil/S948C55540 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pasting cooling copper foil@MB） |  |  | 
Paste the BB nano carbon copper foil as shows as the picture 2
Buckle the RF coaxial cable as shows as the picture 3
1
2

## Slide 6
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
N502-BDD002-010 | Receiver/S938C55975 |  | 1
M109-BDD133-000 | Front housing-ASSY/S948C55798 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Pneumatic machine |  | Press force:5N Dwell time:8S | 
Assemble the receiver as shows as the picture
Press the receiver by Pneumatic machine.
The springs are loaded vertically with two bullets facing down

## Slide 7
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M716-BDD000-000 | P=sensor rubber/S948C55810 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Assemble the P-sensor rubber as shows as the picture 1
1
The big hole side should be assembled in left side
After assembling the P-sensor rubber,inspect it from the side,can NOT see any obvious gap and slant
CCP

## Slide 8
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M501-211413-130 | Screw-1.M1.4X0.30X2.7L/S948C58595 |  | 2
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of lock screws@main board |  | PH000 DriveType 0.8±0.1kgfcm | 
Assemble the main board into the front housing as shows as the picture 1
Drive 2pcs main board screws as shows as the picture 2
1
2
Align the positioning holes of the main board with the positioning pillar of the front cover
2PCS motherboard screws have no leakage lock
CCP

## Slide 9
The front camera FPC is buckled in the motherboard connector, and the buckle is not loose.
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
N706-BDD000-000 | Front camera/S928C55971 |  | 1
M701-BDD000-001 | Shielding cover insulation tape/S948C55833 |  | 2
P316-BC8000-000 | Waterproof label/S948C56754 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Assemble the front camera into the main board as shows as the picture 1
Paste2 PCS shielding cover insulation tape on the shiled cover as shows as the picture 2
Paste 1pcs waterproof label on the earphone socket as shows as the picture 3
1
2
3
Paste2 PCS shielding cover insulation tape to the corresponding position of the shielding cover; do not stick the skew and wrinkle
Place 1 PCS waterproof label on the corresponding position on the earphone socket as shown as the picture

## Slide 10
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
N901-ASH003-000 | Motor/S948C58579 |  | 1
M709-BDD000-011 | Small board connector sealed foam/S948C55531 |  | 1
P316-BC8000-000 | Waterproof label/S948C56754 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of soldering vibrator@sub board |  |  | 
Solder the Motor @sub board,and paste the small board connector sealed foam
Remove the release paper of sub board grounding condtive cloth,and paste waterproof label
Assemble the sub board @front housing and buckle the RF coaxial cable@sub board
1
3. The coaxial RF head is vertically aligned and snapped into the small board RF mount.
2. Remove the sub board grounding conductive cloth release paper;and paste 1pcs waterproof label
2
2
3
2. Assemble the sub board @front housing aligning with the screw hole
2.Paste 1PCS small board connector sealed foam
1.Soldering the vibrator

## Slide 11
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M721-BDD000-002 | Front camera copper foil/S948C55535 |  | 1
M715-BDD000-007 | FPS FPC fixed adhesive/S948C58601 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the heat-dissipatinig copper foil as shows as the picture 1.
Paste the Finger Print FPC fixed adhesive as shows as the picture2
Paste the heat-dissipating copper foil on the back of the front camera and the top of the shield cover. Note: the copper foil can NOT touch the pin of the earphone socket
Align the finger print connector sealed foam and the components to place the FPS FPC fixed adhesive
The FPS FPC fixed adhesive is pasted ahead of the sealed foam,can NOT overlap with the FPS sealed foam,When remove the liner of the FPS adhesive with tweezers,make sure that the tweezers can NOT hit the neighbouring components
Neighbouring components
CCP

## Slide 12
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M709-BDD000-025 | Rear camera conductive sponge/S948C58588 |  | 1
N708-BDV000-000 | 13M rear camera/S928C55973 |  | 1
M716-BDD000-002 | Sub Mic rubber/S948C55812 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the rear camera conductive sponge@rear camera as shows as the picture 1
Place the 13M AF rear camera flat in the fixing slot of the motherboard as shows as picture2.
Assemble the sub Mic silicone sleeve as shows as picture3.
1
2
2
3
Paste the rear camera conductive sponge to the 13M AF
Place the 13M AF rear camera flat in the fixing slot of the motherboard, and install it flat, without lifting, arching
Place the sub -Mic silicon sleeve

## Slide 13
Paste the side key FPC on the corresponding position of the front housing,and insert it into the main board
 |  | Paste the side key FPC and assemble the Ssensor FPC |  |  |  |  |  |  | 
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
N105-BBDB01-010 | Side key FPC/S938C55976 |  | 1
N808-BDD000-010 | Sensor FPCA/S938C55978 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the side key FPC on the corresponding position of the front housing,and insert it into the main board as shows as the picture 1
Assemble the sensor FPC in the slot of the front housing and insert it into the main board as shows as picture2.
1
2
Assemble the sensor FPC in the slot of the front housing and insert it into the main board
CCP
The side key FPC hasn't been assembled into the bottom side totally,NG

## Slide 14
Snap the LCD FPC into the motherboard connector
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
TN PN | Description/Lenovo PN |  | Qty
M716-BDD000-001 | Main Mic rubber/S948C55811 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Snap the LCD FPC into the motherboard connector as shows as the picture 1
Snap the TP FPC connector into the small board connector as shows as the picture2.
Place the main microphone silicone sleeve on the microphone as shows as the picture3.
1
2
2
3
Snap the TP FPC connector into the small board connector and press the connector to ensure that the connector is not loose.
Place the main microphone silicone sleeve on the microphone in the right direction and position
CCP
Spin the vibrator cable by 3 routes,and fix it in the slot,The vibrator cable should NOT be overlapped with the LCD FPC
Hold down the connector to prevent being lifted when pasting the FPC

## Slide 15
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M709-BDD000-027 | FPS grounding conductive sponge/S948C58592 |  | 1
M709-BDD000-002 | FPS support foam/S948C55820 |  | 1
N405-BDD850-000 | FPS module/S928C55803 |  | 1
M701-BDD000-010 | FPS selectrostatic tape/S948C58589 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the fingerprint module grounding conductive sponge and the support foam as shows as the picture 1
Paste the fingerprint electrostatic tape as shows as the picture2.
Assemble the finger print into the main PCBA
1
1
Paste the fingerprint module supports foam according to the shape of the shielding cover. Note: the wrong position, skew, wrinkles, damage, etc.;
Paste the fingerprint module grounding conductive sponge
The fingerprint electrostatic tape is pasted on the FPC steel sheet of the fingerprint module. Be careful not to misplace the position, skew, wrinkles, breakage, etc.
CCP
1
Need to press the FPS FPC area near the connector to activate the FPS adhesive

## Slide 16
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M701-BDD000-005 | Screw hole protective film/S928C56744 |  | 2
N703-BC8000-000 | 2M rear camera/S928C55972 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste 2pcs screw hole protective film,cover two screws on the main board
2. Assemble the 2M FF rear camera into the main board.
Paste 2pcs screw hole protective film,cover two screws on the main board
Place the 2M FF rear camera flat in the fixing slot of the motherboard, and install it flat, without lifting, arching

## Slide 17
Paste 1pcs Earphone socket sealed adhesive
Place the rear camera silicone rubber on the holder of the camera
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M715-BDD000-006 | Earphone socket sealed adhesive@BH/S948C56742 |  | 1
M716-BDD000-003 | Rear camera rubber/S948C55813 |  | 1
M711-BDD000-000 | Speaker anti-dust net/S948C55806 |  | 1
M111-BDD980-000 | Top Back cover/S948C55799 |  | 1
N506-BDD131-000 | Box cover/S948C55800 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
fixture of stick dust gauze@acoustic box |  |  | 
Place the rear camera silicone rubber on the holder of the camera
Paste the speaker dustproof on the bottom back case.
2
2
3
2. Locate the bottom back case and lightly pressed it to make the speaker dustproof net stick to the case
1.Place the speaker dustproof net in the fixture

## Slide 18
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
P316-BC8000-000 | Waterproof label/S948C56754 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Dust-free cloth |  |  | 
Ethanol |  |  | 
Paste 1pcs waterproof label on the back case.
Clean the camera lens adhesive area with dust-free cloth dipped with ethanol
Paste 1pcs waterproof label
Clean the camera lens adhesive area with dust-free cloth dipped with ethanol

## Slide 19
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Dust-free cloth |  |  | 
Ethanol |  |  | 
1.Inspect the connection of LCD FPC connector/Two rear camera connectors,they should
be connected flat and totally
2.Assemble the rear housing
Assemble the rear housing
CCP

## Slide 20
 |  | Drive the device screws 1 |  |  |  |  |  |  | 
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M501-211602-000 | Screw-2.M1.4L3.0/S948C58593 |  | 8
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Automatic Screw Driver |  | T3 DriveType 0.8±0.1kgfcm | 
Drive the device screws -2 by automatic screw driver.
3
.
No screw not fasten well or missing issue.

## Slide 21
 |  | Drive the device screws 2 |  |  |  |  |  |  | 
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M501-211413-130 | Screw-1.M1.4X0.30X2.7L/S948C58595 |  | 6
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Automatic Screw Driver |  | PH0 DriveType 0.8±0.1kgfcm | 
Drive the device screws -1 by automatic screw driver.
3
.
No screw not fasten well or missing issue.

## Slide 22
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M701-BDD000-006 | Front camera protective film/S928C56746 |  | 1
M701-BDD000-012 | Side key protective film/S928C58599 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the front camera protective film as shows as the picture 1
Paste the side key FPC waterproof film as shows as the picture2.
2
1
Paste the front camera protective film
Paste the side key FPC waterproof film

## Slide 23
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M701-BDD000-004 | P-sensor protective film/S928C55533 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Silicone stick |  |  | 
Paste the distance sensor protective film
After pasting the film,need to use the silicone stick to press the distance sensor protective film/Front camera protective film/side key FPC waterproof film to prevent them being lifted.
The distance sensor protective film is attached to the corresponding position on the top of the phone, and it is not skew, wrinkles, and misalignment
CCP

## Slide 24
Stick the camera lens (the smooth side is facing up, the big hole is facing down)
 |  | Paste the camera lens adhesive and camera lens on the back case |  |  |  |  |  |  | 
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M205-BDD132-000 | Camera lens/S948C55808 |  | 1
M715-BDD000-003 | Camera lens adhesive/S948C55822 |  | 1
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Paste the camera lens adhesive on the back case as shows as the picture 1
Stick the camera lens on the back case as shows as the picture2.
1
2
1. The camera lens adhesive is flatly attached to the bottom case limiting slot, without skewing, blocking holes

## Slide 25
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pressing camera len@back cover |  |  | 
Fixture of pressing side key FPC@Front cover |  |  | 
3 in 1 pressing holder |  |  | 
Cylinder camera lens |  | Press force:34N Dwell time:10-12S Diameter:12mm Shore hardness:ShoreA 80 | 
Cylinder side key FPC |  | Press force:31N Dwell time:10-12S Diameter:10mm Shore hardness:ShoreD 85 | 
Press the camera lens and side key FPC by pressing machine.
Machine synchronous press camera lens + side key FPC

## Slide 26
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Finger print pressing head |  |  | 
3 in 1 pressing holder |  |  | 
Cylinder finger print |  | Press force:31N Dwell time:6--8S Diameter:10mm Shore hardness:ShoreD 85 | 
Press the finger print by pressing machine.
The machine press the finger print

## Slide 27
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pasting device label |  |  | 
Fixture of pasting IMEI label |  |  | 
Paste the device label and IMEI label
Paste the device label by fixture
Paste the IMEI label by fixture

## Slide 28
Attention
Operation
Verification
Symbols |  |  | 
Material List |  |  | 
Tinno PN | Description / Lenovo PN |  | Qty
M112-BDD352-000 | Battey cover/S948C57916 |  | 
 | Battery/SB18C53772 |  | 
Tools/ Equipment |  |  | 
Description |  | Parameters | 
Fixture of pasting device label |  |  | 
Fixture of pasting IMEI label |  |  | 
Assemble the battery
2. Assemble the battery cover
Assemble the battery
Assemble the battery cover
Before assemble the battery cover,align the rear camera deco first,then align the finger print
Make sure the finger print area are pressed in position